SkySolve Startup Quick Guide.
For use when skysolve is already installed on an SD card.
### Note: Power off. Do not just pull the power cord.
Instead move the Field/home switch to the opposite side from where it was when booted for the current session. Then watch the green LED inside the case. Wait for it to do an even spaced 9 blinks. Then you can remove the power. Doing otherwise can corrupt the SD card. The switch must be set in the other position for at least 6 seconds before the shutdown sequence will start.

Some units have a switch with three positions. Middle is the same as the Home positions. Left is Field

First install VNC onto a computer that you have. (Called home machine later on.)

To begin with apply power and using the home machine look for wifi skypixxxx. Password is 1234567890

Skysolve should power up running the skysafari listening app and the solving app. Of course the solving will fail until under the stars.

Then attach your home machine to that wifi. Start RealVNC client on your home machine and connect to 192.168.50.5

You may want to add your home wifi network to the PI. There is a script to help you do so. It can be run using VNC to access the RPI operating system GUI. The script is found at directory /skysolve/AccessPopup

On the command line type:
cd /skysolve/AccessPopup
sudo ./installconfig.sh

  Then select 5. You should be able to figure it out from there.

If you want to play with skysove itself. Connect home machine Browser to 192.168.50.5:5000

If you want to see skysolve talk to SkySafari set telescope control in SkySafari to
Scope Type – StellarCat ServoCat
Mount Type – Alt-Az. Push-To

Connect via WIFI
do not select Autop-Detect SkyFi
ip Address 192.168.50.5
Port 5005

It should show you the default position or the one that was last solved.

To play with the GUI click the align button so it does not try to solve. Then play with the camera if you like. Also click the replay images button to see some images I recorded that you can click on the “solve this” not “solve” button. To see it solve individual images. The “solve” button will cycle it through all the history images solveing each as it goes.

The RaspberryPi HQ camera comes with a tiny screw driver used to tighten the C-Mount adapter ring once infinity focus has been adjusted. I have already set the ring to about right. In case you need to adjust and then tighten it. That screw is at the top of the camera lens mount. When looking at the front of the camera it is on the top right hand side of the lens mount.